## Slide 1: Release of the NKG2015 geoid model for the Nordic-Baltic region
J. Ågren, G. Strykowski, M. Bilker-Koivula, O. Omang, S. Märdla, R. Forsberg, A. Ellmann, T. Oja, I. Liepins, E. Parseliunas, J. Kaminskis, L.E. Sjöberg, G. Valsson

## Slide 2: Background
The Nordic Geodetic Commission (NKG) is an association of geodesists from Denmark, Finland, Iceland, Norway and Sweden.
The purpose of NKG is mutual exchange, cooperation and coordination of work with the geodetic infrastructure in the region.
The Baltic countries Estonia, Latvia and Lithuania also take a very active part in the work.
During the years, NKG has computed several gravimetric geoid models:
  NKG1986 (Tscherning and Forsberg 1986)
  NKG1989 (Forsberg 1990)
  NKG1996 (Forsberg et al. 1996)
  NKG2002
  NKG2004
These NKG models have been used as a basis to construct national height corrections models.

## Slide 3
Introduction
The NKG2015 geoid model project started in 2011 with the goal to compute the next official NKG (quasi)geoid model in Nordic and Baltic cooperation
The project has consisted of the following parts:
  Specification (what to do, definitions/conventions on reference systems/frames, permanent tide, postglacial land uplift epoch, etc.)
  Data updates (gravity database, DEM, GNSS/levelling, Ice thickness model)
  Computation (five computation centres, additional gridding investigations)
  Publication (on-going)
The final NKG2015 model is hereby released.
The main purpose of this presentation is to describe he project and the computations that led to the new NKG2015 geoid model.
The model is compared with some other models available over the region.
It is also investigated how much the efforts to transform the GNSS ellipsoidal heights affects the fit of the gravimetric model to GNSS/levelling.

## Slide 4: Initial decisions
The NKG2015 model is a quasigeoid model. This choice was made to be consistent with the national height systems, which are all realisations of EVRS (European Vertical Reference System).
The computation of the gravimetric model and the evaluation using GNSS/levelling is to be made in
  common reference systems/frames for the whole area,
  the postglacial land uplift reference epoch 2000.0,
  and the zero permanent tide system.
All data types are transformed accordingly in the project. (This is not always possible or meaningful, for instance for old, bad gravity data…)
The postglacial land uplift corrections are made using the NKG2005LU model.

## Slide 5: NKG gravity database
Responsible: Gabriel Strykowski, DTU Space.
Has been modernised and is now implemented in PostgrSQL with both a line-based and web-based interface, but still using the same 80-character format as before.
Horizontal positions and heights transformed to national ETRS 89 and EVRS realisations.
Updated with quality checked and new data from all the Nordic and Baltic countries.
Data transformed to zero permanent tide system and epoch 2000.0 (if meaningful considering the accuracy, etc.).
Version 4 delivered June 18, 2016

## Slide 6: Digital Elevation Model (DEM)
Responsible: Mirjam Bilker-Koivula
3’’x3’’ resolution
The Nordic part of the EGG08 DTM complemented with new national models from Finland, Estonia, Latvia and Lithuania.
This means national DEMs in all the Nordic/Baltic countries and SRTM3 or shifted GTOPO30 elsewhere.
Delivered in June 18, 2014

## Slide 7: GNSS/levelling database
Responsible: Ove Omang, Jonas Ågren, Pasi Häkli (transformations)
Levelled heights both in national EVRS realisations and in EVRF 2007.
The GNSS-heights have been transformed to the common ETRS 89 realisation ETRF2000 epoch 2000.0 using the so-called NKG2008 transformations (Häkli et al. 2016).
These transformations consist of a 7-parameter part and a postglacial land uplift correction part (NKG2005LU).
Version 3 confirmed in early 2016 with the publication of Häkli et al. (2016).

## Slide 8: Ice thickness model
Responsible: Ove Omang
Here only for the Norwegian glaciers (to be extended in the future)
Source: Norwegian Water Resources and Energy Directorate (nve.no), transformed and regridded.
Delivered January 12, 2015

## Slide 9
Evaluation of regional geoid computation methods, strategies and software (“The NKG pageant contest” )
Five computations centres:
    Lantmäteriet (LM) - Jonas Ågren
    Tallinn Technical University/Estonian Land Board (TTU/ELB) - Silja Märdla, Artu Ellmann and Tõnis Oja
    DTU Space (DTU) - René Forsberg and Gabriel Strykowsky
    National Land Survey of Finland, Finnish Geospatial Research Institute (NLS-FGI) - Mirjam Bilker-Koivula
    Norwegian Mapping Authority (NMA) - Ove Omang
The task: compute a gravimetric quasigeoid model with epoch 2000.0 and zero tide system using the above data.
It was specified that the following GGMs can be used (converted to the zero tide system),
  GO_CONS_GCF_2_DIR_R5 (Bruinsma et al, 2013), satellite-only
  EIGEN-6C4 (Förste et al, 2014), combined
(Tests have later been made with GOCO05S; see below)
The choice of final computation method (sol. 1a; see next slide) was based mainly on the fit to GNSS/levelling.

## Slide 10
Results from the GNSS/levelling 1-parameter fits

## Slide 11: Method used for the final gravimetric model
LSMSA or KTH method (Sjöberg 1991, 2003,…).
The height anomaly is computed as
  Least squares (stochastic) kernel modification (Sjöberg 1991,…).
Surface gravity anomalies gridded using a Remove-Interpolate-Restore technique, in which
  the gridding was made on the reduced anomaly (reduced for the GGM, RTM, ATM and ICE effects)
  using Least Square Collocation (Geogrid) with individual a priori standard errors (except in Norway where constant 0.5 mGal a priori standard errors are used as is recommended by Märdla et al. 2016). Correlation length is 15 km.
Stokes’ integral evaluated using spherical 1D FFT (Haagmans et al. 1993)

## Slide 12: Reduced gravity anomaly grid
Min | Max | Mean | StdDev | RMS
-85.7 | 84.4 | 0.5 | 11.0 | 11.0
mGal

## Slide 13: Surface gravity anomaly grid
Min | Max | Mean | StdDev | RMS
-135.6 | 200.9 | 4.0 | 23.6 | 24.0
mGal

## Slide 14: Tuning of the least squares modification (stochastic kernel modification)
Unbiased method of Sjöberg (1991)
Spherical integration cap: 2 degrees.
  Signal degree variances computed using the Tscherning and Rapp (1974) model downscaled by the factor 0.5.
  GGM error degree variances set to the formal ones of the satellite-only GO_CONS_GCF_2_DIR_R5 (Bruinsma et al, 2013).
  Four different models to generate terrestrial gravity error degree variances were tested (cf. Ågren et al. 2009):
  LS1: white noise 2 mGal + correlated noise 1 mGal (reciprocal dist., d1/2=0.25 deg.)
  LS2: white noise 1 mGal + correlated noise 0.5 mGal (reciprocal dist., d1/2=0.25 deg.)
  LS3: white noise 0.5 mGal + correlated noise 0.25 mGal (reciprocal dist., d1/2=0.25 deg.)
  LS4: white noise 0.5 mGal + no correlated noise
  The next slide illustrates the signal and error degree variances for LS1 to LS4:
    Red curve: Signal degree variances
    Blue curve: Error degree variances for the GGM
    Black curve: Error degree variances for terrestrial gravity

## Slide 16: Comparison with GNSS/levelling
The crossing degree is here the degree at which the error degree variance of the satellite-only GGM (based on GRACE, GOCE, …) is equal to the error degree variance of terrestrial gravity; cf. the previous slide. (Corresponds to the filtering degree in the Wong and Gore method.)
The best fit to GNSS/levelling is obtained by LS2, which has the crossing degree ~160. This weighting is chosen for the final gravimetric model
It is not so sensitive how the error degree variances in question are chosen.

## Slide 17
GNSS/levelling residuals for the final gravimetric model after a 1-parameter fit/transformation
# | Min | Max | Mean | StdDev
2538 | -0.1740 | 0.1740 | 0.0000 | 0.0285
Normal heights: National EVRS realisations (Nordic), DVR 90 (Denmark) and EVRF2007 (Baltic), (zero tide and epoch 2000.0 except for DK)
GNSS: National ETRS 89 realisations transformed to ETRF2000 epoch 2000.0 and zero tide system.

## Slide 18: Country mean values for the GNSS/levelling residuals
(meter) |  | Before fit | After a common 1-parameter fit of the final gravimetric model |  | 
 | # | Mean | Mean | StdDev | RMS
All | 2538 | -0.4874 | 0.0000 | 0.0285 | 0.0285
Denmark | 675 |  | -0.0184 | 0.0168 | 0.0249
Estonia | 114 |  | 0.0068 | 0.0147 | 0.0161
Finland | 50 |  | 0.0049 | 0.0215 | 0.0218
Latvia | 54 |  | -0.0188 | 0.0246 | 0.0308
Lithuania | 546 |  | 0.0020 | 0.0333 | 0.0333
Norway | 902 |  | 0.0087 | 0.0285 | 0.0298
Sweden | 197 |  | 0.0177 | 0.0186 | 0.0256

## Slide 19: Tests of different transformations for the fit to GNSS/levelling
(meter) | Statistics after a common fit of the final gravimetric model over the whole area |  |  | 
# parameters | Min | Max | Mean | StdDev
1 | -0.2040 | 0.1740 | 0.0000 | 0.0285
3 | -0.2060 | 0.1750 | 0.0000 | 0.0280
4 | -0.2030 | 0.1800 | 0.0000 | 0.0268
The standard deviations are very similar for the 1- and 3-parameter transformations. This shows that the remaining tilt after the permanent tide correction is very small.
That the standard 4-parameter transformation gives a slightly better fit depends mainly on that the residuals in the middle of the area are reduced.
A 1-parameter transformation is preferred for the final model, which gives the best extrapolation outside the GNSS/levelling observations.

## Slide 20
The above gravimetric model is fitted to ETRF2000 epoch 2000.0 and the National EVRS realisations using a 1-parameter transformation.
In order to be able to use the NKG2015 model directly for height determination with GNSS, a permanent tide system correction is included for the GNSS-heights. The following observation equation is used:
which gives the final NKG2015 model:
The gravimetric character of the model is preserved, which means that it is easy for each country to adopt it to GNSS/levelling as they prefer.
Since the above permanent tide correction is included, some would call this a height correction model.
Computation of the final NKG2015 model

## Slide 21: Comparison with other quasigeoid models available over the whole Nordic/Baltic region

## Slide 22
GNSS/levelling residuals for EIGEN-6C4 after a 1-parameter fit/transformation
# | Min | Max | Mean | StdDev
2538 | -0.2340 | 0.1950 | 0.0000 | 0.0421
Normal heights: National EVRS realisations (Nordic), DVR 90 (Denmark) and EVRF2007 (Baltic), (zero tide and epoch 2000.0 except for DK)
GNSS: National ETRS 89 realisations transformed to ETRF2000 epoch 2000.0, converted to the zero permanent tide.

## Slide 23: Difference between NKG2015 and EIGEN-6C4
Correction to the same permanent tide system, mean removed.
Contour intervals: 2 cm for whole area (1 cm in Norway close up).
It is clear that the omission error (above degree 2190) is very significant in Norway.
There are large data dependent differences in some areas, mainly east of Finland and in the Gulf of Finland; see Bilker-Koivula (2015).
Min | Max | Mean | StdDev | RMS
-0.3546 | 0.4183 | 0.000 | 0.0401 | 0.0401
After mean value removal

## Slide 24
Difference between GNSS/levelling and the final NKG2015 model
# | Min | Max | Mean | StdDev
2538 | -0.1740 | 0.1740 | 0.0000 | 0.0285
As explained above, the final NKG2015 model is computed by fitting the final gravimetric model to GNSS/levelling using a 1-parameter fit/transformation and a permanent tide correction to the GNSS heights above the ellipsoid.
Heights: National EVRS realisations (Nordic), DVR 90 (Denmark) and EVRF2007 (Baltic), (zero tide and epoch 2000.0 except for DK)
GNSS: National ETRS 89 realisations transformed to ETRF2000 epoch 2000.0, non-tidal system.

## Slide 25: Illustration of the NKG2008 transformations
Häkli et al. (2016)
The picture shows the difference between
  the national ERS89 realisations and
  ETRF2000 epoch 2000.0.
7-parameter transformation + postglacial land uplift correction (NKG2005LU_abs in the vertical).

## Slide 26
Difference between GNSS/levelling without GNSS transformations and the NKG2015 model
# | Min | Max | Mean | StdDev | RMS
2538 | -0.1950 | 0.1670 | -0.0058 | 0.0272 | 0.0278
Heights: National EVRS realisations (Nordic), DVR 90 (Denmark) and EVRF2007 (Baltic), (zero tide and epoch 2000.0 except for DK)
GNSS: National ETRS 89 realisations, non-tidal system, different postglacial land uplift epochs.
It was not expected that the RMS would be lower without the transformations. The explanation has to be that other error sources counteract the increased GNSS reference frames inconsistencies (including different epochs for the postglacial rebound).
However, note that the distribution of the residuals is rather different, mainly in Sweden and Finland.

## Slide 27: Evaluation of using a different GGM - GOCO05S
Exactly the same method as for the final NKG2015 model.
GNSS/levelling residuals after a 1-parameter shift.
# | Min | Max | Mean | StdDev
2538 | -0.1980 | 0.1620 | 0.0000 | 0.0298

## Slide 28: Difference between the model computed with GOCO05S and NKG2015
Again, exactly the same computation, only difference is GOCO05S (with max. degree 280) vs. GO_CONS_GCF_2_DIR_R5 (max 300)
Contour interval: 1 cm.
Min | Max | Mean | StdDev | RMS
-0.0394 | 0.0404 | 0.0025 | 0.0096 | 0.0100

## Slide 29: Accuracy of the NKG2015 model
In case the standard uncertainties of GNSS and levelling are given, the standard uncertainty of NKG2015 can be derived from the fit standard deviation using the standard law of error propagation,
The different countries have estimated the GNSS and levelling accuracies in somewhat different ways. Here a unified compromise is assumed, which is believed to be reasonably realistic. The relative GNSS/levelling standard uncertainties are set to
  10-15 mm in Denmark and Estonia (small, flat countries with comparatively good data)
  15-20 mm in all the other countries.
  20-25 mm over the whole Nordic/Baltic area (large area, includes remaining uncertainties due to that the different national reference system realisations differ from each other)
It is concluded that the standard uncertainty of the NKG2015 model is at least somewhere around 15-20 mm on land. In areas/countries with good data and a smooth gravity field, the accuracy is higher with a standard uncertainty in the vicinity of 10 mm.

## Slide 30: Conclusions
The final NKG2015 (quasi)geoid model is hereby released.
It has been computed in Nordic/Baltic co-operation in a long term project under the umbrella of NKG (Nordic Geodetic Commission).
The final gravimetric model is computed using the LSMSA method.
The standard deviation in the 1-parameter fit to GNSS/levelling is 2.85 cm, which is significantly better than for previous models.
The relative accuracy of the NKG2015 model is estimated to ~15-20 mm (1 sigma) on land. In some sub-areas (countries), the accuracy is higher (standard uncertainty around 10 mm).
The NKG2015 geoid model will now be used as a basis to compute national height correction models, for instance in Sweden. Since the final model has been fitted to GNSS/levelling with a 1-parameter transformation, and since it also includes a correction between the zero and non-tidal permanent tide systems, it is also directly usable for GNSS height determination.
This is not the end of geoid determination in the NKG area: Right now the main focus is on the Baltic Sea geoid in the EU project FAMOS, for which the NKG2015 will be used as initial reference model (to be checked and improved).
It is the intention to publish this work in two reviewed papers:
  General NKG2015 geoid model paper (Ågren et al. 201X)
  More specialised paper on gravity data gridding (Märdla et al. 2016)

## Slide 31: Extra slide

## Slide 32: Difference between the final NKG2015 model and the preliminary model from March 2016 (WG meeting in Tallinn)
The differences between these two models are the following:
Data updates as decided in Tallinn:
  Data added in several Norwegian fjords and Lake Mjøsa .
  Data corrections in the North Sea
Improved gridding in Norway. The investigations by Silja et al. (2016) clearly show that a more exact interpolation is needed there.
Right now many observations in Norway have the a priori standard error 5 mGal in the NKG DB, which gives a too smooth interpolation around the fjords.
This was solved by using the constant a priori standard error 0.5 mGal in LSC in Norway only. Everywhere else the individual standard errors in the NKG DB are used.
Improved cross validation, with graphical inspection and a higher rejection limit (30 mGal). 116 observations are removed for the final model.
Min | Max | Mean | StdDev | RMS
-0.2575 | 0.2078 | -0.0002 | 0.0065 | 0.0065